Electronic Doorkeeper [Auto Pop Hole opener] VSB

- 30 years - the number one of the world -

opens and closes vertical sliding gates at a hen house, chicken house or similar at dusk. The sensitivity can be adjusted.

VSB

With our quartz-accurate and dust-tight time switches, you may

- open and close at set times or

- open at a set time and close at dusk.

With the aid of an integrated SA automatic closing attachment, the sliding gate may also be closed manually and open automatically at dawn or at a set time on the next morning.

HS

Installation is very simple. Open the sliding gate, fasten it to the VSB unit, insert batteries or plug in the power supply cable, and you are done. When closing, the motor is stopped automatically at the bottom. It is also possible to operate several sliding gates with one VSB unit by using deflexion pulleys or control several VSB units with one time switch. Even the time switches are very easy to install. The contacts are colour-coded.

The VSB unit possesses an electronic overload safety device. All devices are equipped with extremely rugged housings. The electronic system is protected against aggressive gases, moisture and dirt with a special fired varnish on the bottom of the printed circuit board in SMD technology. If you want to install the VSB unit in the hen house, you will need an AS ambient light sensor.

The VSB unit is weatherproof and does not open during lightning.

We use extremely durable structural elements exclusively and expect them to work at least two (2) decades.

Electronic Doorkeepers [Auto Pop Hole controllers] by AXT-electronic are deployed around the globe,

from cold Canada through to Australia’s hot Outback.

Specifications of VSB electronic gate control unit:

VSB dimensions (WxHxD):  125 mm (4,9“) L/R, 125 mm (4,9“) high, 75 mm (2,9“) F/B

Operating voltage	     :   6...12 V DC

Batteries 		     :   4 type AA (LR 6) batteries; battery-life: 1 to 4 years

Weight, of sliding gate 	     :   200 g, minimum;  3kg, maximum

Stroke length        	     :   60 cm, maximum; adjusts automatically

Operating time       	     :   About 40 seconds for 50 cm

Prices, incl. 19 % VAT:

Product  Description

VSBb	  including four AA-size batteries (Battery life 1-4 years) for outdoor installation,     	     €  106

opens and closes at dawn and dusk. For installation inside the henhouse, see AS.

BS-D	  digital battery time switch for 1-3 VSBb, 2 AA batteries, lifetime approx 6 years 	     €    46

protective casing & cable for several VSB units

For indoor installation:

AS	  outside light sensor is required when installing the VSBb within a hen house.	     €      8

HS	  Vertical sliding gate for hens, approx. 22 L/R x 33 cm high (9“x13“) with sliding-splint   €    20

mHS	  i.e. for ducks 30x40cm								      €    21

gHS	  i.e. for goose 33x50cm								      €    23

UR	  Idler, to lift several HS´s with one VSB…                                                         	      €      2

UR2	  Idler for special using, see at mounting examples				     	      €    10

Three year guarantee

Payment by VISA or MasterCard  (Please send your card number and it´s date of expiry and CVC2 (Card Validation Code)= the last three digits of the card no. inside the signature box on the back of the card), PayPal

or by bank transfer.

Automatic Feeder

for poultry, birds, cats, dogs, etc with a battery-powered motor, very easy to programme, for dry feed (grain, round pellets max. 10mm Ø).

The feeding times can be programmed very easily, e.g. 3 times a day. If the amount has almost been eaten up, the less tasty elements are also eaten. This machine will allow you to provide less feed for other animals like mice, sparrows or the like.

Technical data:

Feeding times:     the time can be programmed down to every quarter hour.

delivery time:       from 1 second, adjustable in second Rates, output ca. 30g/s, approx. 300g/10s

Batteries              4 AA (Mignon) with a serviceable life of 1-5 years.

FA1-5  Feeding silo approx. 5 litres. For 1 - 3 animals, e.g. quails, hens, cats, dogs. 		€ 179.00

The feed drops out of the funnel into a container placed beneath it (not supplied).

Diameter approx. 180mm, height approx. 370mm

FA1-10 Works like FA1-5. Feed silo approx. 10 litres. Height approx. 570mm 		€ 188.00

FA2-5  During the feed process, the feed trickles into the feed channel    			€ 188.00

Feed silo approx. 5 litres. Diameter of the feed channel approx. 360mm.

Diameter of the silo approx. 180mm. Height approx. 370mm.

FA2-10  Works like FA2-5. Feed silo approx. 10 litres. Height approx. 570mm. 		€ 199.00

| FA1 | FA2 |
| --- | --- |

It is easy to extend the silo cylinder, e.g. to 20 litres, or connect it to other containers.

_____________________________________________________________________

AXT-Electronic  *   Wartburgstrasse 10  *   D-99817 Eisenach / Germany

Tel. 0049 3691 721070  Fax 0049 3691 721080      www.axt-electronic.eu